## Slide 1
數位控制系統期末專題 – Final Project Report Lateral Dynamic Control of a Civil Passenger Aircraft with Discrete LQR Controller
組員
R07921006 楊軒昱
R07921012 張峻豪

## Slide 2: Outline
Part 1. References
Part 2. Introduction
  Problem formulation
  System Assumption
  Aircraft System Description
  Controllability and Observability
Part 3. Continuous Time system
  Continuous Time Controller
  Simulation Performance
Part 4. Discrete Time system
  Zero-Order Hold Emulation Design
    Plant Variables
    Simulation Performance
  First-Order Hold Emulation Design
    Plant Variables
    Simulation Performance
Part 5. Summary of Simulation

## Slide 3: Part 1. References

## Slide 4: References
[1: Ashraf et al. 2018]
  Adnan Ashraf1, Wu Mei, Liu Gaoyuan, Zeeshan Anjum and Mian Muhammad Kamal , “Design Linear Feedback and LQR Controller for Lateral Flight Dynamics of F-16 Aircraft,” in Proceedings of International Conference On Control Automation & Information Sciences (ICCAIS), Hangzhou, China, pp. 367~371, October 24-27, 2018.
[2: Livet et al. 1994]
  T. Livet, F. Kubica and J.F Magni , “Performance improvement by feedforward: application to civil aircraft control design,” in Proceedings of IEEE International Conference on Control and Applications, Glasgow, UK, Aug. 24-26, 1994.
[3: Liu & Jiao 2010]
  A. Schirrer, C. Westermayer, M. Hemedi and M. Kozek, “LQ-based design of the inner loop lateral control for a large flexible BWB-type aircraft,” in International Conference on Control Applications, Yokohama, Japan, Sep. 8-10, 2010.

## Slide 5: References
[4: Usta et al. 2011]
  M. Ali Usta, Ömür Akyazı and A. Sefa Akpınar , “Aircraft roll control system using LQR and fuzzy logic controller,” in International Symposium on Innovations in Intelligent Systems and Applications, Istanbul, Turkey, pp. 367~371, Jun. 15-18, 2011.
[5: Bai & Dong 2013]
  Bin Bai and Chaoyang Dong, "Modeling and LQR Switch Control of Morphing Aircraft," in International Symposium on Computational Intelligence and Design, Hangzhou, China, Oct. 28-29, 2013.
[6: Rajeswari & Suresh 2015]
  V. Rajeswari and L.Padma Suresh, “Comparative Assessment of the performances of Linear Quadratic and Sliding Mode Control Methodologies in the Control of Lateral Axis of Aircraft,” in Proceedings of International Conference on Circuit, Power and Computing Technologies (ICCPCT), Cebu, Philipines, pp. 1-6, March 27-28, 2015.

## Slide 6: References
[7: Wang et al. 2016]
  Kangle Wang, Shaoping Wang, Xingjian Wang and Zhongwei Yang, “Active fault-tolerant control strategy for lateral motion of civil aircraft,” in IEEE International Conference on Aircraft Utility Systems (AUS), Beijing, China, Oct. 10-12, 2016.
[8: Liu & Jiao 2017]
  Baoxu Liu and Zongxia Jiao, “LQR Lateral-Directional Control Law Design for Distributed Propulsion Layout Flying Wing,” in Proceedings of IEEE International Conference on CIS & RAM, Ningbo, China, pp. 715~719, Nov. 19-21, 2017 .
[9: Hasan & Khan 2018]
  Ehtisham ul Hasan and Amna Khan, "Lateral acceleration control of aircraft using PID, linear quadratic regulator (LQR) and linear quadratic integral (LQI); A comparative case study," in International Conference on Electrical and Electronic Engineering (ICEEE), Istanbul, Turkey, May 3-5, 2018.
[10: Shin et al. 1985]
  K.G. Shin, C.M. Krishna, Y.-H. Lee, "A unified method for evaluating real-time computer controllers and its applications," IEEE Transactions Automatic Control, Vol. 30, No. 4, pp. 357-366, April 1985.

## Slide 7: Part 2. Introduction

## Slide 8: Introduction
The dynamics of many aircraft can be modeled as two sets of essentially decoupled multivariable systems.
  The first subsystem is called the longitudinal dynamics.
  The second subsystem is called the lateral dynamics, which is our simulation topic of this project.
The lateral dynamics concerns the motion of the craft in roll and yaw caused by the action of the ailerons and rudder.

## Slide 9: Introduction (Cont.)
The lateral dynamics are further subdivided into two parts:
  Roll dynamics: roll rate and roll angle
  Yaw dynamics: yaw rate and side-slip rate
Fig. An aircraft angle control system.
[Ref: https://slideplayer.com/slide/4569242/]

## Slide 10: Problem formulation
We want to design the controllers for the lateral dynamics of an A340 airline in normal cruise flight.
First, we establish a continuous time system model
  The control method we used in this project is state feedback control (SFC).
  The controller of the model was designed by using LQR control. [1: Ashraf et al. 2018]
  The continuous model is regarded as the ground truth when comparing with the discrete time system model.
Then, we discretized the continuous system with different sampling time and sampling methods.
After that, we design the controllers of the discrete time system model in different situation and compare the performance with continuous time system model.

## Slide 11: System Assumption
There is no coupling between the lateral dynamics and the longitudinal dynamics.
The rudder and aileron deflections are limited to approximately to ±10°.
The plant dynamics are only estimated of the actual value. (The numerical values are referred to the homework of linear system theory)

## Slide 12: Aircraft System Description
State-Space model in continuous time
Where
  (Upper limit = 0.2, Lower limit = -0.2)
  (Sine wave: Amplitude = 0.5, Frequency = 0.2 Hz)
  (Square wave: Amplitude = 0.1, Frequency = 0.1 Hz)
The limit of rudder and aileron deflections are ± 10°, which is approximately ± 0.2 rad.

## Slide 13: Aircraft System Description (Cont.)

## Slide 14: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(A), ctrb(A,B) and obsv(A,C), respectively.
rank(A) = 4 → The matrix is full rank → The system is stable
rank(ctrb(A,B)) = 4 = rank(A) → The matrix is full rank → The system is controllable
rank(obsv(A,C)) = 4 = rank(A) → The matrix is full rank → The system is observable

## Slide 15: Part 3. Continuous Time System

## Slide 16: Continuous time system (SFC)
The controlled output z is the same as the measured output y, so that in the standard notation E=C.
Controllers to be designed

## Slide 17: Continuous time controller
We calculate the parameters of the controller K and Kr via LQR control
By MATLAB command,
  K_lqr = lqr(A,B,Q,R)
  Kr_lqr = -(E*((A-B*K_lqr)^-1)*B)^-1
  Where Q = eye(4) and R = 0.01*eye(2)
Therefore, we can get

## Slide 18: Lateral Velocity Results in Continuous Time
Fig. Reference (Yellow dotted line) and Output state (White)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 19: Roll Angle Results in Continuous Time
Fig. Reference (Yellow dotted line) and Output state (White)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 20: Part 4. Discrete Time system

## Slide 21: Zero-Order Hold Emulation Design

## Slide 22: Discrete time system (ZOH)
Zero-Order hold is added

## Slide 23: Plant Discretization and Discrete Controller
We can discretize the system and design the discrete time controllers by the following MATLAB command:
  Ts = 0.2; % Setting sampling time h
  sys = ss(A, B, C, []); % State-space model in continuous time
  sys = c2d(sys,Ts, ‘zoh'); % Transform the continuous system into discrete form in h
  [F,H,C_dis,D_dis] = ssdata(sys); % Obtain the discrete state-space model
  K_lqr_dis = lqrd(A,B,Q,R, Ts); % Discrete model lqr
  Kr_lqr_dis = -(E*((A-B*K_lqr_dis)^-1)*B)^-1 % Discrete model lqr

## Slide 24: Discretized Plant (ZOH, Ts = 0.2s)

## Slide 25: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 26: Lateral Velocity Results in Sampling Time = 0.2 sec
Fig. Reference (Yellow dotted line) and Output state (Red)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 27: Roll Angle Results in Sampling Time = 0.2 sec
Fig. Reference (Yellow dotted line) and Output state (Red)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 28: Discretized Plant (ZOH, Ts = 1.0s)

## Slide 29: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 30: Lateral Velocity Results in Sampling Time = 1.0 sec
Fig. Reference (Yellow dotted line) and Output state (Blue)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 31: Roll Angle Results in Sampling Time = 1.0 sec
Fig. Reference (Yellow dotted line) and Output state (Blue)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 32: Discretized Plant (ZOH, Ts = 2.0s)

## Slide 33: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 34: Lateral Velocity Results in Sampling Time = 2.0 sec
Fig. Reference (Yellow dotted line) and Output state (Green)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 35: Roll Angle Results in Sampling Time = 2.0 sec
Fig. Reference (Yellow dotted line) and Output state (Green)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 36: Lateral Velocity Results in Different Sampling Time
Continuous Time
Sampling Time = 0.2 s
Sampling Time = 1 s
Sampling Time = 2 s
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2

## Slide 37: Lateral Velocity Results in Different Sampling Time (Cont.)
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 38: Roll Angle Results in Different Sampling Time
Sampling Time = 1 s
Sampling Time = 2 s
Continuous Time
Sampling Time = 0.2 s
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1

## Slide 39: Roll Angle Results in Different Sampling Time (Cont.)
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 40: First-Order Hold Emulation Design

## Slide 41: Discrete time system (FOH)
First-Order hold is added

## Slide 42: Discretized Plant (FOH, Ts = 0.2s)

## Slide 43: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 44: Lateral Velocity Results in Sampling Time = 0.2 sec
Fig. Reference (Yellow dotted line) and Output state (Red)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 45: Roll Angle Results in Sampling Time = 0.2 sec
Fig. Reference (Yellow dotted line) and Output state (Red)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 46: Discretized Plant (FOH, Ts = 1.0s)

## Slide 47: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 48: Lateral Velocity Results in Sampling Time = 1.0 sec
Fig. Reference (Yellow dotted line) and Output state (Blue)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 49: Roll Angle Results in Sampling Time = 1.0 sec
Fig. Reference (Yellow dotted line) and Output state (Blue)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 50: Discretized Plant (FOH, Ts = 2.0s)

## Slide 51: Stability, Controllability and Observability
To check the stability, controllability and observability of the system, we can use MATLAB command rank(F), ctrb(F,H) and obsv(F,C_dis), respectively.
rank(F) = 4 → The matrix is full rank → The system is stable
rank(ctrb(F,H)) = 4 = rank(F) → The matrix is full rank → The system is controllable
rank(obsv(F,C_dis)) = 4 = rank(F) → The matrix is full rank → The system is observable

## Slide 52: Lateral Velocity Results in Sampling Time = 2.0 sec
Fig. Reference (Yellow dotted line) and Output state (Green)
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 53: Roll Angle Results in Sampling Time = 2.0 sec
Fig. Reference (Yellow dotted line) and Output state (Blue)
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1
Fig. Control Input
(upper bound: 0.2, lower bound: -0.2)

## Slide 54: Lateral Velocity Results in Different Sampling Time
Continuous Time
Sampling Time = 0.2 s
Sampling Time = 1 s
Sampling Time = 2 s
Reference: sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2

## Slide 55: Roll Angle Results in Different Sampling Time (Cont.)
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 56: Roll Angle Results in Different Sampling Time
Continuous Time
Sampling Time = 0.2 s
Sampling Time = 1 s
Sampling Time = 2 s
Reference: square wave (magnitude: 0.1 , Frequency: 0.1)
State Initial condition: 1

## Slide 57: Roll Angle Results in Different Sampling Time (Cont.)
Reference Signal sin wave (magnitude: 0.5 , Frequency: 0.05)
State Initial condition: -2
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 58: Part 5. Summary of Simulation

## Slide 59: Analysis (zoh)
Fig. Lateral Velocity Reference and Output State
Fig. Roll Angle Reference and Output state
From the results of lateral velocity and roll angle, it is obviously that the shorter the sampling time is, the better the system tracks the reference signal. However, the results of discrete controller can’t still be as good as continuous controller.
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 60: Analysis (foh)
Fig. Lateral Velocity Reference and Output State
Fig. Roll Angle Reference and Output state
From the results of lateral velocity and roll angle, we can discover that as the sampling time is shorter, the system tracks the reference signal better. Nonetheless, the results of discrete controller can’t still be as good as continuous controller.
On the other hand, because some of the input signals are cut off by the input constraints when the sampling time = 0.2s, the system output becomes tremble.
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 61: Comparison of zoh and foh
By comparing the performance of zoh and foh, we can find out that zoh performs better than foh because the input signal is cut off by input constraints in our cases
Fig. Roll Angle Reference and Output State (zoh)
Fig. Roll Angle Reference and Output State (foh)
White line for continuous time
Red line for sampling time = 0.2 sec
Blue line for sampling time = 1.0 sec
green line for Sampling time = 2.0 sec

## Slide 62: Comparison of zoh and foh (Cont.)
Fig. Control Input of roll angle control in sampling time = 0.2 s (zoh)
Fig. Control Input of roll angle control in sampling time = 0.2 s (foh)
Fig. Control Input in continuous time
First-order-hold in MATLAB uses the slope at the sampling instance to fill up the period between the next sampling instance.
zoh vs. foh Ref: https://ww2.mathworks.cn/help/control/ref/c2d.html

## Slide 63: Comparison of zoh and foh (Cont.)
Fig. Control Input of roll angle control in sampling time = 2 s (zoh)
Fig. Control Input of roll angle control in sampling time = 2 s (foh)
Fig. Control Input in continuous time
However, foh might occur severe error if the slope changes dramatically during sampling period with long sampling time.
Thus, zoh performs much better than foh when the sampling time is long.
zoh vs. foh Ref: https://ww2.mathworks.cn/help/control/ref/c2d.html